Steps Before First Engine Start

Weight and Balance computed

Prop Blade Tracking

Log entry needed?  I think yes in builders log

Remove Upper and Lower Cowls

Remove Prop Spinner

Spark Plugs

Remove and Gap

Use Copper Crush Washers

Use Anti Seize on plug threads

Torque to Specs

Attach Spark Plug Wires

Clean springs with MEK.

Do not over-tighten – finger tight plus 1/8” more

Install Oil Filter (torque value?)

Safety Wire Oil Filter

Add appropriate amount and type of Oil to engine (mineral oil 7-8 qts)

Fuel Gauge Calibration

Check EIS4000 manual

Fuel system Pressure Test

Fill Both Fuel tanks

Battery Master – Off

EIS – On

EFIS 1 – On

Engine monitor page

Fuel Selector – Right

Boost Pump – On

Verify and Note Stable Fuel Pressure

Boost Pump – Off

Check each fitting for fuel by sight and smell

Fuel Selector – Left

Boost Pump – On

Verify and Note Stable Fuel Pressure

Boost Pump – Off

Check each fitting for fuel by sight and smell

Battery Master – Off

EFIS 1 – Off

EIS – Off

Fuel Flow Test

Make sure fuel system is not still pressurized from prior test

Disconnect fuel supply hose at FI servo

Make hose connection via a union to some 3/8” tubing

Tubing should empty to a measured vessel of at least 5 Gallons

Tie tail to the ground simulating climb attitude

Begin Timing (3 minutes)

Boost Pump – On

Wait 3 minutes

Boost Pump – Off

End Timing

Calculate GPH

Note in logbook?

Unusable fuel amount Check

Return aircraft to level attitude

Pump remaining fuel from both tanks via Boost Pump into measured containers

Periodically shake wing to loosen debris

Note difference between quantity pumped into tank and fuel pumped out, That is the unusable fuel

Reconnect Fuel Supply Hose at FI servo.

Fuel Filter/Fuel Tank Contaminant Check

Drain remaining unusable fuel from tanks via fuel drains – remove drains if necessary

Remove Fuel filter, remove filter element and clean

Re-install Fuel element and filter back into airplane.

Replace Fuel Drains if Removed

Oil System Air Purge

Remove bottom 4 spark plugs

Disconnect oil hose from oil pressure transducer

Connect via a union a piece of 3/8” tubing to direct oil flow

Battery Master – On

Left Ignition – Off

Right Ignition – Off

Throttle – Closed

Mixture – Cutoff

Starter – On

Crank Engine until oil is seen coming out of tubing

20 second cranks

2 minute intervals

Re-connect oil hose to oil pressure transducer

Replace and torque bottom plugs

Clean up oil mess

Engine Start Proceedure.

Have at least one other person to help

Provide with Hand Held radio – Frequency: 123.45 for handheld and aircraft

Verify handheld operation

Provide Fire Extinguisher to helper

Notepad and Pen for Helper to note read back values of Oil pressure and Fuel Pressure

Have Fire Extinguisher in cockpit.

Communication

“Shutdown Now” – self explanatory

“Looks Good” – self explanatory

Secure everything loose on the plane – fairings, cover panels, etc.

Fuel Aircraft to half capacity

Secure aircraft to vehicle, building or something immovable

Chock wheels

Brakes - On

Engine Start

Throttle – Closed

Mixture – Cutoff

Fuel Selector – Left

Boost Pump – On

Confirm and Note Stable Fuel Pressure

Mixture – Rich

5 seconds

Mixture – Cutoff

Boost Pump – Off

Throttle – Cracked Open

Battery Master – On

EIS – On

EFIS 1 – On

Wait till unit stabilized

Page to Engine Page

Comm 1 – 123.45

Verify Communications with Helper

Left Ignition – On

Right Ignition – On

E-Bus Alternate Feed - Off

Starter – Engage

When engine fires

Mixture – Rich

Throttle 1000 – 1100 RPM

Monitor Oil Pressure (60 to 110 PSI )

Note Actual Oil Pressure – Read to Helper

Cylinder Temps

EGT – climbing

CHT – slowly climbing

Verify for all four cylinders

One to Two minutes for all to Stabilize and continue rising

Oil Temperature

Climbing to 90F

Note System Voltage and system Amps

Throttle

1300 RPM – 5 Seconds

Note Oil Pressure

1400 RPM – 5 Seconds

Note Oil Pressure

1500 RPM – 5 Seconds

Note Oil Pressure

1600 RPM – 5 Seconds

Note Oil Pressure

1700 RPM – 20 Seconds

Prop

Cycle – Briskly pull prop control back (3-5 Seconds Max)

Watch for RPM drop

Manifold Pressure Rise

Oil pressure Drop

Push Prop Control back in when above conditions happen

Prop may not cycle until 2nd or 3rd attempt.

If Unsuccessful, try to cycle Prop at 1800 RPM

Magneto Check

Left Ignition - Off

Verify and Note RPM Drop

Left Ignition – On

Wait 20 Seconds

Right Ignition – Off

Verify and Note RPM Drop

Right Ignition - On

Wait 20 Seconds

Throttle Back to Idle

Note Idle RPM

Mixture - Lean

Slowly pull mixture and note RPM increase when leaning

Do this to confirm Idle Mixture adjustment

Master Swith – Off

engine should not quit

Mixture – Cutoff

Throttle – Closed

Left Ignition – Off

Right Ignition – Off

Fuel Selector – Off

Look over engine and prop hub carefully, Checking for Leaks or problems

Have a beer, or two.